## Slide 1
Mean Absolute Error (MAE)
MAE = (1/N) sum_i |T_i^PINN - T_i^FEM|
Main accuracy metric. It is reported as mean-window MAE over the prediction windows.
Relative L2 Error
Rel. L2 = ||T_hat - T_FEM||_2 / ||T_FEM - T_w||_2
Full-field error, normalised by the temperature change above the water bath. Here T_w = 20 deg C.
FEM Anchor Reduction
R(k) = (1 - N_win(k)/20) x 100%
Efficiency metric. It shows how many FEM anchor calls are saved when the PINN predicts longer windows.
How I read the numbers
MAE: average temperature error in deg C.
Relative L2: spatial field quality at 30 s.
R(k): saved FEM solver calls.
Together, they show the trade-off between accuracy and computational cost.
Important note from the report
Final-window MAE alone can be misleading in PINN-only tests.
Near 30 s, the field naturally moves toward the water temperature.
So the mean-window MAE is used as the primary metric.
Source: Chapter 3, Evaluation Metrics.
Evaluation Metrics
BENCHMARKS AND METRICS
UiA | University of Agder
Master Thesis Defense
25