## Slide 1
The project begins with an industrial A356 aluminium quenching problem and asks whether Finite Element Method (FEM) time-step calls can be reduced without losing useful temperature accuracy.
Reference paper
The reference study models water quenching of cast A356 automotive subframes. Its FEM simulation gives the industrial motivation: temperature gradients during quenching drive distortion.
Our approach
We keep the same physical process setting, but test a different route: FEM provides anchor snapshots and NAS-PINN predicts selected intermediate windows.
Validation path
Because the real industrial data arrived late, the workflow starts with controlled surrogate geometries and then moves toward more complex 3D and Thermal Fin benchmarks.
Material
A356
aluminium
Initial T
540 C
hot part
Bath T
20 C
water
Quench
30 s
transient
Goal
skip FEM
with anchors
Intro: What We Do in This Project
INTRODUCTION
UiA | University of Agder
Master Thesis Defense
3