## Slide 1
How many FEM solver calls can be replaced by PINN predictions while keeping temperature error within engineering limits?
We built
A FEM-anchored NAS-PINN framework that predicts intermediate thermal fields while FEM snapshots remain the correction source.
We tested
Fixed-k, adaptive-k and PINN-only modes were evaluated from simple 2D domains to complex 3D and Thermal Fin cases.
We measured
MAE, relative L2 error, skip-factor schedule and FEM-call reduction are reported together.
Error limits
Geometry-dependent thresholds: 10 C for canonical 2D; 15 C for 3D and Thermal Fin.
Engineering tolerance calculation
Delta T = T0 - Tw = 540 C - 20 C = 520 C | 15 C / 520 C = 0.0288 = 2.9% approx. 3% | 10 C / 520 C = 1.9%
Research Question and Contributions
INTRODUCTION
UiA | University of Agder
Master Thesis Defense
7